Linux Host
This section show how to install a new operating system to your DragonBoard™ 410c using the fastboot method on a Linux host computer.

- Step 1: Make sure fastboot is set up on host computer
- Step 2: Connect host computer to DragonBoard™ 410c
- Step 3: Boot DragonBoard 410c into fastboot mode
- Step 4: Flash Bootloader
- Step 5: Recall location of all downloaded files
- Step 6: Unzip all files
- Step 7: Flash all files to the DragonBoard™ 410c
- Step 8: Reboot DragonBoard 410c

Step 1: Make sure fastboot is set up on host computer.
You can install fastboot from source or using your distro package manager.
From source:
  - Android SDK “Tools only” for Linux can be downloaded here
  - The Linux “Tools Only” SDK download does not come with fastboot, you will need to use the Android SDK Manager to install platform-tools.
  - To do this follow the “SDK Readme.txt” instructions included in your SDK “Tools Only” download.
- If you are still having trouble setting up fastboot, click here for a short tutorial video
          - Or using a distro package manager:
  # Red Hat flavour (Fedora, CentOS)
  $ sudo yum install android-tools
  # Debian (Ubuntu)
  $ sudo apt-get install android-tools

Step 2: Connect host computer to DragonBoard 410c
- DragonBoard™ 410c must be powered off (unplugged from power)
- Make sure microSD card slot on DragonBoard™ 410c is empty
- S6 switch on DragonBoard™ 410c must be set to ‘0-0-0-0’. All switches should be in “off” position
- Connect USB to microUSB cable from host computer to DragonBoard™ 410c
Step 3: Boot DragonBoard™ 410c into fastboot mode
Please read all bullet points before attempting
- Press and hold the Vol (-) button on the DragonBoard™ 410c, this is the S4 button. DragonBoard™ 410c should still NOT be powered on
- While holding the Vol (-) button, power on the DragonBoard™ 410c by plugging it in
- Once DragonBoard™ 410c is plugged into power, release your hold on the Vol (-) button.
- Wait for about 20 seconds.
- Board should boot into fastboot mode.
From the connected host machine terminal window, run the following commands:
# Check to make sure device is connected and in fastboot mode
$ fastboot devices
Typically it will show as below
de82318 fastboot
At this point you should be connected to your DragonBoard™ 410c with a USB to microUSB cable. Your DragonBoard™ 410c should be booted into fastboot mode and ready to be flashed with the appropriate images.
Step 4: Flash Bootloader
- Use host computer
- Open "Terminal" application
- Recall location of Bootloader download.
- The bootloader file should be named dragonboard410c_bootloader_emmc_Y-XX
- Y represents Android or Linux
- XX represents the release number of the Bootloader
- cd to the directory with your unzipped Bootloader Folder
$ cd <extraction directory>

#Example:
cd /Users/YourUserName/Downloads
#<extraction directory> = /Users/YourUserName/Downloads
#For this example we assume the "Bootloader" is in the Downloads folder.

$ cd <unzipped Bootloader folder>

#Example:
cd dragonboard410c_bootloader_emmc_linux-40
#<unzipped Bootloader folder> = dragonboard410c_bootloader_emmc_linux-40
#This example took place during release 40

# This command will execute the flashall script within the bootloader folder
$ ./flashall
The bootloader has now been flashed to the eMMC. Rebooting will launch the newly-flashed boot loader, which will allow us to flash the remaining parts of the operating system.
# Reboot the system so we can flash the rest.
$ sudo fastboot reboot
Step 5: Recall location of all downloaded files
Recall location of all downloaded files from the downloads page, files will be different for Android and Linaro/Debian:
Linaro/Debian: Recall location of boot and rootfs downloaded from the downloads page
- You should have downloaded the boot file
- You should have downloaded ONE of rootfsfile (EitherDeveloperorDesktop - ALIP` version)
Android: Recall location of boot.img.tar.xz, system.img.tar.xz, userdata.img.tar.xz, recovery.img.tar.xz, persist.img.tar.xz, cache.img.tar.xz, downloaded from the downloads page
All of these files should have been downloaded from the downloads page
Step 6: Unzip both files
Step 7: Flash all images to the DragonBoard 410c
- Use host computer
- Use "Terminal" application
- Recall location of extracted(unzipped) files
- cd to the directory with your unzipped files
- From within extraction directory, execute the following commands:
Linaro/Debian:
# (Once again) Check to make sure fastboot device connected
$ sudo fastboot devices
# It will show similar to below if the device is connected successfully
de82318 fastboot
# cd to the directory the boot image and were extracted
$ cd <extraction directory>
# Make sure you have properly unzipped the boot and rootfs downloads
$ sudo fastboot flash boot boot-linaro-jessie-qcom-snapdragon-arm64-**BUILD#**.img
$ sudo fastboot flash rootfs linaro-jessie-developer-qcom-snapdragon-arm64-**BUILD#**.img
Note: Replace BUILD# in the above commands with the file-specific date/build stamp.
Android:
# (Once again) Check to make sure fastboot device connected
$ sudo fastboot devices
# It will show similar to bellow if the device is connected successfully
de82318 fastboot

# cd to the directory with extracted images
$ cd <extraction directory>

# Make sure you have properly unzipped the downloads
$ sudo fastboot flash boot boot.img
$ sudo fastboot flash system system.img
$ sudo fastboot flash userdata userdata.img
$ sudo fastboot flash recovery recovery.img
$ sudo fastboot flash persist persist.img
$ sudo fastboot flash cache cache.img
Step 8: Reboot DragonBoard™ 410c
- Unplug power to DragonBoard™ 410c
- Unplug micro USB cable from DragonBoard™ 410c
- Ensure HDMI connection to monitor
- Ensure keyboard and/or mouse connection (Depending on your rootfs selection)
- Plug power back into DragonBoard™ 410c
- Wait for board to boot up
- Board will boot into either command line or desktop depending on rootfs
Note: For Linaro/Debian the username and password are both “linaro” when the login information is requested.
Congratulations! You are now booting your newly installed OS directly from eMMC on the DragonBoard™ 410C